## Slide 1
FIELD REPORT
Building Sovereign SIGINT
Signals intelligence, AI, and infrastructure you actually own

## Slide 2
OVERVIEW
What We'll Cover
What “sovereign AI” actually means, and why it matters for SIGINT specifically
Choosing the models: a task-driven lineup, not one model doing everything
Understanding the hardware: HackRF and RTL-SDR in real depth
Two workflows: browser-based (OpenWebRX+) and manual (GNU Radio)
The Occupancy concept — turning raw RF energy into queryable data
Real lessons learned, pulled directly from an actual build

## Slide 3
CONCEPT
Local by Default, Cloud by Exception
Every model, reference dataset, and signal capture lives on hardware the operator physically controls
A local LLM (via Ollama) handles the overwhelming majority of queries — summarization, cross-referencing, natural-language lookups
Cloud AI is not forbidden — it remains a deliberate, opt-in escalation path for sanitized, non-sensitive queries only
Matters most in exactly the environments this tool is built for: financial, defense, and critical-infrastructure contexts

## Slide 4
THE CORE PRINCIPLE
“The point isn't to reject cloud AI. It's to make sending data outward a conscious choice, not a silent default.”

## Slide 5
WHY AI + SIGINT
Three Capabilities the Pairing Is Built to Enable
Natural-language spectrum queries — “what's been active on 20 meters”, answered live from logged activity (working: the radiod producer feeds the occupancy DB continuously from live HF, and a native tool lets the local LLM query it and answer with real signals; a companion VHF/UHF producer exists in code but isn't wired as a service yet)
A second AI source, different in kind: Kismet WiFi capture (APs, clients, MACs, SSIDs, signal) via its own native tool over kismetdb — kept in device-centric shape, not flattened into occupancy; semi-live via a 15-min refresh
A third AI source — reference, not observation: a mirrored signal-ID catalog (hundreds of signals with frequency, mode, modulation, bandwidth, description) via a native tool (lookup by name, search by characteristic). Occupancy + Kismet say what is present; SigID says what it is — and paired with the vision model, triage an unknown by shape, cross-check the catalog, confirm by measured frequency
Vision-assisted signal identification — comparing a captured waterfall against a reference catalog of known signal types
Summarization of long capture sessions — turning a shift's worth of detections into a short, readable brief
None of this requires the AI to understand RF physics — it requires retrieval, comparison, and language, which is exactly what current local models do well

## Slide 6
DEEPEST TECHNICAL SECTION
Choosing the Models: Three Jobs, Three Models
qwen3:14b
General Reasoning
~9.3 GB
Talks to the operator: answers questions, summarizes activity, reasons across multiple observations.
nomic-embed-text
Retrieval Backbone
~274 MB
Embeds every reference document and corpus entry for RAG — the smallest model, doing the least glamorous but most essential job.
gemma3:12b
Vision
~8.1 GB
The only model that can look at an image — comparing a captured spectrogram against known signal shapes, as triage, not final ID.

## Slide 7
DESIGN RATIONALE
Why Not One Larger Model
VRAM: a single model excellent at reasoning, embeddings, AND vision at once likely won't fit in 16GB alongside everything else the box runs
Embeddings specifically benefit from a model trained and evaluated for that exact task — a repurposed chat model rarely matches a purpose-built embedder at the same size
Ollama loads one model at a time — three right-sized models that swap in and out beats one oversized generalist sitting in VRAM regardless of whether the current task needs it
Transferable lesson: choose models by the job, not by leaderboard ranking

## Slide 8
DEEPEST TECHNICAL SECTION
Understanding the Hardware
RTL-SDR
Originally a $5 DVB-T TV tuner dongle, repurposed by the community into a general-purpose receiver
R820T tuner covers ~24MHz–1.7GHz natively (with a gap ~1.1–1.25GHz)
RTL-SDR Blog v3/v4: HF reception via direct sampling mode — no hardware mod, but bypasses tuner amplification
Gain must live in the correct config location — confirmed the hard way
HackRF One
Wide range: ~1MHz–6GHz, at coarser 8-bit resolution
Half-duplex — transmit or receive, not both at once
The generalist: one device reasonably capable across VHF, UHF, and well beyond
A stock antenna can silently invalidate a calibration — suspiciously identical readings across two different bands was the clue; the fix was a proper resonant antenna, not code

## Slide 9
THE MOST INSTRUCTIVE BUG
RX-888 MkII — Diagnosing the Wrong Layer
Symptom: brand-new RX-888 stuck at USB2 (480M), never USB3 (5000M) — needs USB3 to work at all
Chased: every port, two cables, a full BIOS audit, and a USB3 PCIe card purchase — all reasonable, all wrong
Actual cause: the Cypress FX3 powers up in DFU/bootloader mode and enumerates at USB2 BY DESIGN — it only jumps to USB3 AFTER firmware is uploaded. Every test ran against a device that couldn't yet show the behavior being tested
Proof it worked all along: once firmware loaded, 486 MB captured in ~8s (~60 MB/s — impossible over USB2)
Lesson: a symptom that looks like hardware can be device-state; ask whether the thing is even in a state where the wanted behavior is possible BEFORE replacing hardware

## Slide 10
THE PAYOFF
RX-888 + radiod — Why It Matters for AI
radiod brings up 18 simultaneous demodulated channels from ONE wideband HF capture — WWV, FT8, APRS, CW, voice — each a network multicast stream
For a single narrow channel, the three SDRs are peers to the AI; only the RX-888 feeds it EVERY HF band at once, continuously, with no sweeping blind spots
So it matters MORE for the AI/occupancy mission than for the interactive waterfall it was originally bought for
Single-owner device: time-shares between radiod (always-watching AI) and OpenWebRX+ (interactive human waterfall) via an explicit mode switch

## Slide 11
WORKFLOWS
Two Ways to Actually Work With Signals
OpenWebRX+ (Browser-Based)
Live, multi-user, browser-accessible waterfall and audio
Built-in decoders: Packet/APRS, LoRa, FLEX/POCSAG, FT8 and related digital modes
Its own Feature Report page states plainly why any capability is or isn't available — a genuinely well-designed diagnostic tool
Best for live, human-facing monitoring
Manual (GNU Radio)
Flowgraphs built directly against hardware via gr-osmosdr, one interface for multiple device types
Full control: energy detection, feature extraction, triggering a raw capture
Where genuinely custom SIGINT logic lives — no off-the-shelf decoder required
Best for unattended, custom detection logic

## Slide 12
THE OCCUPANCY CONCEPT
Turning RF Energy Into Queryable Data
Standard spectrum-management terminology: is a frequency in use, over what window, for how long — not what the signal IS
Signal identification is a separate, optional layer built on top of an occupancy record, not baked into it
Design reference: Kismet's proven DEVICES/PACKETS split — a long-lived aggregate plus a lean, high-volume event log
Real adaptation required: RF signals generally lack the durable identity a MAC address gives a WiFi device — frequency (binned) + mode substitutes

## Slide 13
WHY CALIBRATION MATTERS
“A calibrated threshold, not a guessed one, is what separates a genuinely useful occupancy log from a noisy one.”

## Slide 14
REAL-WORLD LESSON
Enumeration Is Not Validation
A device showing up in a list, or a package installing without error, proves far less than it appears to. This build required a real, sustained data capture or a real end-to-end flowgraph execution before considering any component actually working — because several real bugs (a USB permission gap, a missing secondary dependency, a rate limit) were invisible to a simple installed-successfully check and only surfaced when something real was actually run.

## Slide 15
REAL-WORLD LESSON
Test as the User Who Will Actually Need It to Work
A permission validated correctly for one system user was silently assumed to also cover a completely different system user created later by a separate service's own install process. The two accounts had no inherent relationship; proving access worked for one proved nothing about the other. Any permission check is only as good as the identity it was actually tested under.

## Slide 16
REAL-WORLD LESSON
A Suspiciously Clean Result Deserves More Suspicion Than an Error
An outright failure announces itself. A calibration reading that returns without error but happens to be identical across two physically different situations is a quieter, easier-to-miss signal that something is wrong. The habit worth building: sanity-check a clean result against physical expectation, not just whether the tool reported success.

## Slide 17
MORE REAL LESSONS
Additional Principles From the Build
Recoverable failure should be handled as recoverable — a single rate-limit response once aborted an entire multi-hour sync; the fix treated it as the expected condition it actually was
Flag what's actually confirmed, not what's a reasonable guess — an unconfirmed assumption, stated honestly with a safe fallback, beats false confidence
Version drift is a recurring category of bug — a renamed package, an unsupported config key, a systemd unit type that behaves differently than assumed, all wearing different clothes for the same underlying failure

## Slide 18
Sovereign by Design
A local AI stack that never depends on a cloud connection to function — validated by real hardware at every step, honest about what still needs building.