## Slide 1
LAB 6
Phase 6.1 — ka9q-radio (RX-888 HF Ingest)
Wideband capture, many simultaneous channels, and a cross-phase permission gap
Sovereign SIGINT — College Lab Series

## Slide 2
SESSION OVERVIEW
Learning Objectives
1
Understand radiod's wideband-capture-plus-channelization architecture
2
Explain why this build deliberately does NOT route RX-888 through OpenWebRX+
3
Diagnose a permission gap between two different system users

## Slide 3
CONCEPT
What Makes radiod Different
radiod captures the ENTIRE HF spectrum at once and simultaneously demodulates many independent channels from that single wideband capture — no other tool in this stack does that
Each configured channel (WWV and other time/beacon signals receivable at your site, ham bands, a wideband IQ tap) publishes as its own IP multicast stream — any downstream tool can subscribe independently (note: Canada's CHU shut down 22 Jun 2026 — pick beacons you can actually receive)
This multicast architecture is exactly what later phases (SigMF export, occupancy tracking) need to consume RX-888 data without re-architecting anything

## Slide 4
SYSTEM DESIGN
radiod vs OpenWebRX+ — one device, two roles
The RX-888 is a single-owner USB device: exactly one process can hold it. radiod (this phase) is the AI/occupancy path — many simultaneous channels published for arbitrary downstream consumption. OpenWebRX+ is the interactive human waterfall — one signal at a time, but a beautiful full-HF panorama
Both are legitimate; they TIME-SHARE the hardware via scripts/rx888-mode.sh (ai | interactive | status), which stops the other owner and waits for USB release before switching. 'ai' (radiod) is the always-watching default; 'interactive' hands it to OpenWebRX+ and pauses AI HF occupancy
Key insight on value: for a SINGLE narrow channel the three SDRs are peers to the AI, but only the RX-888 (via radiod) can feed the AI EVERY HF band at once, continuously, with no sweeping blind spots — so it matters MORE for the AI mission than for the waterfall it was originally bought for
There is no clean native path for OpenWebRX+ to consume radiod's streams (radiod emits demodulated PCM / a raw-IQ format OpenWebRX+ can't ingest) — hence time-sharing, not simultaneous sharing

## Slide 5
DESIGN RATIONALE
Key Design Decisions
radiod's own system user ('radio') is created by its own install process, separate from any interactive human user
Firmware path handling is explicitly best-effort — verified against radiod's own startup log, not assumed
FFTW wisdom generation started back in Phase 2 pays off here — radiod's own high-effort planning has a head start

## Slide 6
HANDS-ON
Hands-On Lab (requires RX-888 MkII)
1
sudo ./scripts/phase6-ka9q-radio.sh
2
./scripts/phase6-ka9q-radio-validate.sh — a real pcmrecord capture from a live channel, not just service-active status
3
Verify firmware loaded correctly by checking radiod's own startup log
4
Subscribe to a multicast channel manually and confirm real audio/IQ data is flowing

## Slide 7
REAL-WORLD BUG
Real Bug: A Source Build That Broke on a Driver You Don't Use
On the first real-hardware run, the ka9q-radio build failed hard: 'fobos.c:16: fatal error: fobos.h: No such file'. A recent ka9q-radio 'main' had pulled the Fobos SDR driver (fobos.c) into the DEFAULT build path — but per ka9q's own notes it should only compile with 'make FOBOS=1', it needs third-party libfobos headers that aren't installed, and no Fobos device is present. The fix that the whole ka9q ecosystem uses: pin to a known-working commit (e1224dcd, the one projecthorus/auto_rx pins) rather than tracking a fast-moving main branch. Once pinned, everything that had been FLAGGED as risky worked on the first proper attempt: radiod uploaded the RX-888 firmware itself, the device re-enumerated to USB3, the dedicated 'radio' system user's USB permissions worked (a cross-user permission gap we'd anticipated but which resolved cleanly), 18 demodulators started, and validation captured 716 KB of real WWV 10 MHz AM audio. The lesson: pinning a source dependency to a tested commit is not paranoia — a fast-moving upstream WILL break your default build path eventually, on a component you don't even use.

## Slide 8
BEFORE MOVING ON
Exit Criteria (all confirmed on real hardware)
radiod active, demodulators started (WWV, 20m/40m FT8, APRS, CW, LSB/USB, wideband-iq — channel list is site-specific), no firmware errors
A real pcmrecord capture succeeds from a live multicast channel (confirmed: 716 KB of WWV 10 MHz AM audio)
The 'radio' system user has confirmed USB access — and the RX-888 re-enumerated to USB3 (5000M) after radiod loaded its firmware

## Slide 9
GROUP DISCUSSION
Discussion Questions
Q1
Why is pinning a source dependency to a tested commit worth the loss of 'latest' — and what class of failure does tracking a moving 'main' expose you to?
Q2
The RX-888 is a single-owner device shared between radiod and OpenWebRX+. How do you design a safe switch that can't leave both fighting for the hardware?
Q3
Why is 'many simultaneous channels from one capture' architecturally different from 'many separate captures,' and what does that make possible for AI occupancy that a swept narrowband SDR cannot?

## Slide 10
NEXT SESSION
Phase 6.2 — Decode Layer: GNU Radio, direwolf, multimon-ng, and the system-Python venv boundary.