## Slide 1
LAB 8
Phase 6.3 — SigID Mirror
A local signal-identification reference catalog
Sovereign SIGINT — College Lab Series

## Slide 2
SESSION OVERVIEW
Learning Objectives
1
Build an incremental local mirror of an external signal-identification wiki
2
Understand why this uses live incremental sync rather than a one-time static import
3
Diagnose and fix a real rate-limiting failure

## Slide 3
CONCEPT
What Gets Mirrored, and Why Locally
sigidwiki.com catalogs several hundred known RF signal types — frequency ranges, modulation notes, waterfall images, audio samples
Mirrored locally so this reference material is available for AI-assisted signal identification WITHOUT a live internet dependency at query time — consistent with this course's sovereign-AI philosophy
A live MediaWiki API sync, not a one-time archive dump — designed to be re-run periodically and pick up only what's changed

## Slide 4
SYSTEM DESIGN
Incremental Sync Design
Bootstrap run: enumerate the entire wiki (namespace 0)
Subsequent runs: query only pages changed since the last successful sync
Per-page revision ID and per-file content hash both tracked in a local manifest — the same idempotency pattern as Phase 5's ingest pipeline
Rate-limited deliberately (a fixed delay between requests) and uses an honest, identifiable User-Agent — respectful use of someone else's public infrastructure

## Slide 5
DESIGN RATIONALE
Key Design Decisions
Runs as a weekly systemd timer, not continuously — this reference data doesn't change fast enough to justify more frequent syncing
~589 signals mirrored, including images and audio samples, not just text metadata
The API endpoint location is auto-discovered rather than hardcoded, since not every wiki install exposes api.php at the same path

## Slide 6
HANDS-ON
Hands-On Lab
1
./scripts/phase6-sigid-mirror.sh (no sudo — this is a long-running first sync, expect 30-50+ minutes)
2
Monitor progress in the terminal or run it detached (nohup ... &) and check back
3
./scripts/phase6-sigid-mirror-validate.sh — confirms real content landed in /data/reference/sigid
4
Browse a few synced entries and confirm images/audio downloaded correctly alongside the text

## Slide 7
REAL-WORLD BUG
Real Bug: One Rate-Limit Response Killed the Entire Run
On the real, live bootstrap sync (hundreds of pages, each potentially with several image downloads), the external wiki's server returned an HTTP 429 (Too Many Requests) partway through — and the original code treated any non-success HTTP response as fatal, aborting the entire multi-hour sync and losing all remaining progress. But a rate-limit response across a run making hundreds of API calls is an EXPECTED, recoverable condition, not an exceptional one. The fix added retry-with-backoff, honoring the server's own Retry-After header when it provided one, applied consistently across both the metadata API calls and the separate file-download code path (which had originally been on its own unprotected route, a second bug found by inspecting the fix's own blast radius). The re-run after the fix completed cleanly: 497 pages, 834 files, dozens of 429s all handled gracefully instead of fatally.

## Slide 8
BEFORE MOVING ON
Exit Criteria
A full or incremental sync completes without a fatal error
/data/reference/sigid contains real metadata, images, and audio
Re-running the sync correctly performs an incremental update, not a full re-download

## Slide 9
GROUP DISCUSSION
Discussion Questions
Q1
Why should a rate-limit response be treated differently from most other HTTP error codes?
Q2
What's the ethical dimension of scraping/mirroring a public wiki's content — what did this build do to be a 'good citizen' of that infrastructure?
Q3
If this sync needed to run against ten different wikis with ten different rate-limit policies, how would you generalize the retry logic?

## Slide 10
NEXT SESSION
Phase 6.4 — OpenWebRX+: a browser-based SDR receiver, and a feature dependency that wasn't obvious from its error message.