## Slide 1
LAB 9
Phase 6.4 — OpenWebRX+
A browser-based SDR receiver, with two real, non-obvious feature bugs
Sovereign SIGINT — College Lab Series

## Slide 2
SESSION OVERVIEW
Learning Objectives
1
Deploy OpenWebRX+ as the browser-facing SDR receiver for HackRF and RTL-SDR
2
Use OpenWebRX+'s own Feature Report as a self-diagnosing tool
3
Diagnose two real, genuinely non-obvious configuration issues

## Slide 3
CONCEPT
What OpenWebRX+ Provides
A live, multi-user, browser-based waterfall and audio receiver for HackRF and RTL-SDR — and, via an added SoapySDDC driver, the RX-888 for a full 0-30 MHz HF panorama (the RX-888's original purchase rationale; time-shared with radiod, see Phase 6.1)
Built-in digital-mode decoders: Packet/APRS (via direwolf, Phase 6.2), LoRa, FLEX/POCSAG (via multimon-ng), FT8/FT4/JS8, and more
SDR device profiles configure center frequency, mode, and gain per use case — deliberately left as a manual web-UI step in this build, not scripted, given how fragile getting these settings wrong can be

## Slide 4
SYSTEM DESIGN
The Feature Report
http://<host>:8073/features lists every optional capability and states explicitly why it's unavailable if it is — a genuinely well-designed self-diagnosis tool
Worth checking BEFORE configuring a profile that depends on a decoder that isn't actually present, rather than debugging blind from the live UI
A feature can depend on MULTIPLE underlying requirements — as this build discovered directly

## Slide 5
DESIGN RATIONALE
Key Design Decisions
Installed AFTER Phase 6.2's decode tools deliberately, so direwolf/multimon-ng auto-detection happens correctly at OpenWebRX+'s own first startup
Gain lives in the per-profile settings, not the live receiver panel's gain control — confirmed the hard way
RTL-SDR v3/v4 boards support HF reception via direct sampling mode, no hardware modification needed — a fact worth knowing given RTL-SDR's native tuner range starts around 24MHz

## Slide 6
HANDS-ON
Hands-On Lab
1
sudo ./scripts/phase6-openwebrx.sh
2
sudo openwebrx admin adduser <username> — create your own admin account
3
Check http://<host>:8073/features BEFORE configuring any profile
4
Add HackRF and/or RTL-SDR device profiles via Settings -> SDR devices
5
Confirm a live waterfall and audio, then try Packet/APRS on 144.390 MHz

## Slide 7
REAL-WORLD BUG
Real Bugs: A Silent Waterfall, a Two-Part Feature, and a Case-Sensitive Driver
Bug 1 — a real waterfall showed faint signals despite a live antenna: RF gain lives in per-profile Settings, not the live panel's Gain control (which doesn't persist). Bug 2 — Packet/APRS was missing though direwolf showed YES in the Feature Report; the real gate was a SECOND requirement, aprs_symbols (NO), not even in the package repo — needing a git clone. Bug 3 (adding the RX-888 later) — a three-part snag: (a) the SoapySDDC driver's source build failed on 'make all' because its unittest target doesn't compile on Ubuntu 24.04 — but the actual driver module built fine, so building the specific targets and installing the .so directly into SoapySDR's module dir worked; (b) the OpenWebRX+ device showed 'State: unknown' and SoapySDRUtil --probe gave 'no match' — because the driver key is CASE-SENSITIVE: the factory registers as 'SDDC' (capital), so 'driver=sddc' fails and 'driver=SDDC' works; (c) 'SoapySDRUtil --find' was the tool that revealed the exact device string. Shared lesson across all three: when something 'isn't there,' the authoritative move is to ask the tool what it actually sees (Feature Report, --find), not to guess from the symptom.

## Slide 8
BEFORE MOVING ON
Exit Criteria
OpenWebRX+ service is active and reachable via browser
A configured SDR device shows a live waterfall with a real, distinguishable signal
Packet/APRS decode produces real decoded packets on 144.390 MHz

## Slide 9
GROUP DISCUSSION
Discussion Questions
Q1
Why is checking a documented Feature Report more reliable than guessing from a live UI's symptoms?
Q2
What's the difference between a device not having enough gain versus a device not being properly connected — how would you tell them apart faster next time?
Q3
Should a feature-flag system report ALL of a feature's unmet dependencies at once, or just the first one it finds? What are the tradeoffs?

## Slide 10
NEXT SESSION
Phase 6.5 — SigMF Writer: exporting raw IQ captures to an open, interoperable standard.