## Slide 1
LAB 10
Phase 6.5 — SigMF Writer
Exporting raw IQ captures to an open, interoperable format
Sovereign SIGINT — College Lab Series

## Slide 2
SESSION OVERVIEW
Learning Objectives
1
Understand the SigMF standard for signal metadata and IQ recordings
2
Write raw IQ captures from RX-888, RTL-SDR, and HackRF into SigMF format correctly
3
Confirm correctness via real hardware captures, not just synthetic test data

## Slide 3
CONCEPT
What SigMF Is, and Why It Matters
An open, community standard for describing recorded RF signal data — a metadata JSON file paired with a raw binary IQ data file
Interoperable with external tools (IQEngine, GNU Radio's own SigMF blocks) — signal captures made in this project can be analyzed elsewhere without a custom format
This is the layer that closes a real gap identified earlier: NEITHER radiod NOR OpenWebRX+ can export raw IQ — only decoded/demodulated output. This writer is the only path to a raw, reprocessable capture in this whole build

## Slide 4
SYSTEM DESIGN
Three Different Native Hardware Formats
RX-888 (rx888_stream): 16-bit signed IQ (ci16_le)
RTL-SDR (rtl_sdr): unsigned 8-bit IQ (cu8), offset-binary, centered at 127.5 not 128
HackRF (hackrf_transfer): signed 8-bit IQ (ci8)
Each format needs DIFFERENT normalization math before it's a valid SigMF recording — getting the offset wrong introduces a DC-offset artifact, not an obvious crash

## Slide 5
DESIGN RATIONALE
Key Design Decisions
A single capture-to-sigmf.sh utility wraps the device-specific capture tool AND the SigMF writer into one command, auto-selecting the correct input format per device
All three formats convert to complex64 internally — a real, acknowledged tradeoff (up to 8x file-size increase for the 8-bit formats) versus preserving native bit depth
An extra_capture_metadata hook exists in the writer specifically so a future SigID match or occupancy-DB record can be embedded directly in a capture's metadata

## Slide 6
HANDS-ON
Hands-On Lab
1
./scripts/phase6-sigmf-writer.sh (venv setup, no sudo)
2
./scripts/phase6-sigmf-writer-validate.sh — round-trips synthetic data through all three formats
3
./scripts/capture-to-sigmf.sh --device rtlsdr --freq <a known frequency> --sample-rate 2048000 --duration 5 --output-name my_test
4
Inspect the resulting .sigmf-meta file: confirm frequency, sample rate, and SHA512 hash are all correct

## Slide 7
REAL-WORLD BUG
Catching an Overconfident Claim Before It Shipped
Early in writing this module, the code asserted a specific library method name for setting author/description metadata as if it were confirmed, when it had only been guessed by pattern-matching against similar libraries. That guess was caught and flagged honestly in the code BEFORE ever running against real hardware — a documented 'this is unconfirmed, here's a graceful fallback if it's wrong' comment, rather than a confident but untested claim. When a real hardware capture was finally run, the guess turned out correct — but the discipline of flagging it as unconfirmed until actually tested, rather than presenting confidence that hadn't been earned yet, is the transferable lesson, independent of whether that particular guess happened to be right.

## Slide 8
BEFORE MOVING ON
Exit Criteria
Synthetic round-trip tests pass for all three formats (ci16_le, cu8, ci8)
A real hardware capture from at least one device produces a valid SigMF recording
The written metadata's SHA512 hash matches an independent verification

## Slide 9
GROUP DISCUSSION
Discussion Questions
Q1
Why does an open standard like SigMF matter more for a SIGINT tool than a proprietary internal format would?
Q2
What's the practical cost of the 8-bit-to-complex64 conversion, and when would preserving native bit depth actually matter?
Q3
How do you decide when a claim in your own code is 'confirmed' versus 'a reasonable guess that hasn't been tested yet'?

## Slide 10
NEXT SESSION
Phase 6.6 — Occupancy Database: a Kismet-inspired schema, and turning raw signal energy into structured data an LLM can query.