## Slide 1
LAB 11
Phase 6.6 — Occupancy Database
A Kismet-inspired schema, and turning RF energy into queryable data
Sovereign SIGINT — College Lab Series

## Slide 2
SESSION OVERVIEW
Learning Objectives
1
Design an occupancy database schema using Kismet's proven pattern as a reference, not a standard to copy blindly
2
Understand the real adaptation needed when RF signals lack a durable identity the way MAC addresses give WiFi devices
3
Run and calibrate the two real occupancy producers — radiod (continuous HF) and the device-flexible HackRF/RTL-SDR key-frequency producer (on-demand VHF/UHF) — that actually populate the database

## Slide 3
CONCEPT
What 'Occupancy' Means Here
Standard RF/spectrum-management terminology: is a given frequency in use, over what time window, at what duration — not signal classification, not raw detection, specifically frequency+time+duration of use
No single existing standard defines a machine-readable RECORD format for this the way SigMF standardizes IQ captures
Kismet's kismetdb schema is the closest real, proven precedent — not because it's a broad interoperability standard (it isn't; other tools consume Kismet's EXPORTS, not its native format directly), but because its DEVICES/PACKETS split is a directly analogous, battle-tested pattern

## Slide 4
SYSTEM DESIGN
signals + sightings, Adapted From DEVICES + PACKETS
sightings (-> Kismet's PACKETS): one row per detection event — lean columns for fast queries
signals (-> Kismet's DEVICES): a long-lived aggregate, keyed by frequency (binned) + mode — substituting for the durable MAC address identity that RF signals generally don't have
Paired epoch-seconds + milliseconds timestamp fields, matching Kismet's actual convention (mirrors C's tv_sec/tv_usec struct split) — deliberately NOT a single combined millisecond integer
Zero dependencies beyond the Python standard library — any future producer, regardless of venv or system-Python context, can call directly into it

## Slide 5
DESIGN RATIONALE
Key Design Decisions
SQLite with WAL journaling + busy_timeout, so multiple producers write concurrently without contention — this is what lets radiod stream continuously while the on-demand VHF/UHF producer writes at the same time
FREQUENCY_BIN_HZ (a placeholder value) determines how close two reported frequencies must be to count as 'the same signal' — explicitly flagged as needing real-world tuning, not asserted as correct
Two producers actually populate the DB, each calling the same record_sighting(): radiod (continuous, ~17 demodulated HF channels, first to populate it) and one device-flexible key-frequency producer that drives either the HackRF (primary, Comet GP-1 antenna) or the RTL-SDR (backup, broadband antenna) on-demand for VHF/UHF. The older GNU Radio single-frequency monitors were never hardware-validated and are superseded by this producer.
Each producer/device carries its OWN calibrated threshold, because each has a different noise floor and even opposite gain behavior — see the calibration lesson below

## Slide 6
HANDS-ON
Hands-On Lab
1
./scripts/phase6-occupancy-db-validate.sh — confirms schema, frequency-binning, and aggregate tracking with real functional tests
2
Confirm the continuous radiod occupancy producer is running (systemd --user radiod-occupancy.service) and has populated the DB — this is the source that first filled it
3
Run the VHF/UHF key-frequency producer on-demand against real hardware: python3 decode/vhf_uhf_key_freq_producer.py --device hackrf --once --verbose (or --device rtlsdr) — observe the per-channel dBFS readings and the quiet/ACTIVE split
4
Query occupancy.db directly and inspect a signals row's aggregate first_seen/last_seen/total_sightings
5
Install the occupancy native tool in Open WebUI (see docs/openwebui-setup-guide.md) and ask the local LLM a natural-language question — e.g. 'Call query_occupancy near 10 MHz' — closing the capture->DB->AI loop

## Slide 7
REAL-WORLD BUG
Real Lessons: Calibration Is Where the Truth Lives
Calibrating three different devices taught the same discipline from several angles. First, suspiciously identical readings across two very different bands were the diagnostic clue that something other than real noise was being measured — traced to a continuous carrier being read as if it were background, and separately to an antenna inadequate for the frequency; the fix for the latter was a proper resonant antenna (a 2m/70cm vertical), NOT code. Second, the two SDRs discriminate at OPPOSITE gain extremes: the HackRF's power readout clamps near -30 dBFS below high gain (so it only separates signal from floor at LNA 40+), while the RTL-SDR compresses at high gain and works best at MINIMUM gain — a single 'sensible' gain guess would have been wrong for one of them. Third, a single reference sample misleads: the RTL-SDR's first sweep looked alarmingly busy until three sweeps revealed the true floor and one genuine transmission standing well above it. The through-line: don't trust a calibration number because the tool ran without error — sanity-check against physical expectation, calibrate per device against its own floor, and take multiple samples before believing any of them.

## Slide 8
BEFORE MOVING ON
Exit Criteria
Occupancy DB schema applies cleanly and passes its functional test suite
The radiod producer is confirmed populating the DB continuously; the VHF/UHF key-freq producer runs on-demand and shows a sane quiet/ACTIVE split against its calibrated per-device threshold
The occupancy native tool answers a natural-language question from real DB data in Open WebUI — the capture->DB->AI loop is closed end to end

## Slide 9
GROUP DISCUSSION
Discussion Questions
Q1
Why doesn't a fixed-size frequency bin work equally well for a 125kHz LoRa channel and a 20MHz WiFi channel?
Q2
What real-world antenna or RF-path problem would produce two suspiciously identical noise-floor readings at very different frequencies?
Q3
If you had to extend this schema to also track signal BANDWIDTH occupancy, not just center frequency, what would you add?

## Slide 10
NEXT SESSION
Final Lab — Use Cases of Sovereign SIGINT: putting the whole stack to work, and previewing the final project.