## Slide 1
FINAL LAB
Final Lab — Use Cases of Sovereign SIGINT
Putting the whole stack to work
Sovereign SIGINT — College Lab Series

## Slide 2
SESSION OVERVIEW
Learning Objectives
1
Synthesize all six build phases into real, applied SIGINT use cases
2
Understand how the AI stack augments raw capture — via native in-process tools that let the local LLM query THREE live sources (occupancy, Kismet WiFi devices, the SigID reference catalog) in natural language
3
Walk the end-to-end unknown-signal identification workflow that ties those sources together
4
Preview the final project

## Slide 3
CONCEPT
What the Full Stack Actually Enables
Raw RF capture (radiod continuous HF, plus on-demand VHF/UHF key-frequency producers) feeding a local occupancy database of what's actually on the air, when, and for how long
SigMF-format archival captures for anything worth deeper offline analysis, interoperable with external tools
A local, sovereign AI layer that reasons over what's been observed WITHOUT any cloud dependency — and reaches the data through NATIVE in-process Open WebUI tools, the reliable path for local models (external HTTP/OpenAPI tools proved unreliable to invoke; that lesson is part of the story)
THREE live AI sources, each in its native shape: RF occupancy (what's active), Kismet WiFi device intelligence (what devices are present), and the SigID reference catalog (what a signal IS) — observation plus reference, all queryable in natural language
Most of this was built and validated independently across the prior sessions; this session combines them and adds the native-tool query layer that turns separate databases into things one local model reasons across

## Slide 4
SYSTEM DESIGN
Example Use Case Walkthroughs
Spectrum situational awareness: the occupancy native tool answering 'what's been active on 20m recently' in natural language — a working live query against the DB, not a summary of a stale export
Unknown-signal identification (the flagship workflow): measure frequency/bandwidth on your receiver, have the vision model (gemma3:12b) describe the waterfall's shape, then — switching to the tool-capable model (qwen3:14b) — search the SigID reference tool by that shape and near that frequency, and confirm by triangulation (shape + frequency + bandwidth must agree). Vision alone is triage; vision + SigID + measured frequency is a defensible first ID. See docs/vision-signal-identification-guide.md.
WiFi device intelligence: the Kismet native tool lets the LLM answer 'what access points were seen, with SSIDs and signal' from real capture — a different KIND of intelligence (device/protocol presence) than frequency occupancy, kept in its own native shape
Physical security / asset discovery: Ubertooth and Evil Crow RF would extend this same sovereign-AI philosophy into Bluetooth/BLE and sub-GHz ISM bands — a genuinely different SIGINT domain (hardware groundwork laid in Phase 1; not yet wired into the AI layer)
Emergency communications awareness: Winlink/APRS traffic monitoring entirely on infrastructure you control, relevant to ARES/RACES-style operations

## Slide 5
DESIGN RATIONALE
What Makes These 'Sovereign' Rather Than Just 'Local'
No use case in this list requires an internet connection to function at query time — the SigID reference, the AI models, and the occupancy history are all already on the box
Cloud LLMs remain available as a deliberate, opt-in escalation path for non-sensitive queries — not a silent default dependency
This distinction matters most exactly where this course's audience works: environments where sending RF/signal data to a third party is not an acceptable default, regardless of how good that third party's model is

## Slide 6
HANDS-ON
Hands-On Lab
1
Choose one use case from today's walkthrough and reproduce it end-to-end on your own build
2
Document which phases of the stack you relied on, and which, if any, you found yourself wanting to extend
3
Identify one genuine limitation you hit that wasn't covered in a prior lab session
4
Group discussion: compare use cases chosen across the class

## Slide 7
REAL-WORLD BUG
A Course-Wide Reflection, Not a Single Bug
Every prior lab session in this course documented a REAL failure encountered on real hardware — package renames, cross-user permission gaps, rate limits, gain settings, calibration sanity checks. None of these were manufactured for teaching purposes; they are the literal record of building this system once, honestly, with the mistakes included. The transferable skill this course has been teaching, session by session, isn't any single fix — it's the discipline of validating with a REAL test at every step, treating a suspicious result as a reason to dig deeper rather than move on, and being honest in your own documentation about what's confirmed versus what's still a guess. That discipline is what separates a system that happens to work once from one you can actually trust.

## Slide 8
BEFORE MOVING ON
Exit Criteria for the Course
Can articulate, end-to-end, how a signal goes from antenna to an AI-answerable question in this system — including the native-tool query layer that closes the loop
Has reproduced at least one complete use case on their own build — ideally the unknown-signal identification workflow across the vision and tool-capable models
Is prepared to scope and propose a final project building on this foundation

## Slide 9
GROUP DISCUSSION
Discussion Questions
Q1
Which single phase of this build do you think has the most direct application to your own professional or research context?
Q2
Where would you draw the line between 'local by default' and 'cloud by exception' if you were deploying this in a real organization?
Q3
What SIGINT use case would you want to pursue that this course's current architecture does NOT yet support?

## Slide 10
NEXT SESSION
Final Project (to be assigned) — building on this foundation.