## Slide 1
LAB 1
Phase 1 — Hardware & Drivers
Standalone validation before any application layer
Sovereign SIGINT — College Lab Series

## Slide 2
SESSION OVERVIEW
Learning Objectives
1
Install and validate SDR hardware drivers independently of any consuming application
2
Understand why RX-888 requires a fundamentally different install path than HackRF/RTL-SDR
3
Run real capture tests, not just device enumeration
4
Use the device-selection menu to install only the hardware you have

## Slide 3
CONCEPT
Why Standalone Validation?
Every SDR application (GNU Radio, OpenWebRX+) links against the same shared driver library — HackRF via libhackrf, RTL-SDR via librtlsdr
Proving the driver/USB layer works BEFORE any application touches it means a later failure is known to be a software/config issue, not a hardware one hiding underneath
Enumeration (lsusb) is not proof of a working device — this course requires a real, sustained data capture at each phase

## Slide 4
SYSTEM DESIGN
The RX-888 Exception
HackRF and RTL-SDR: one shared driver library, every application links against it
RX-888 MkII has NO shared driver library — two entirely separate codebases (rx888_stream for validation, radiod for actual SIGINT ingest) each talk to raw USB directly, each loading firmware onto the device's Cypress FX3 chip
CRITICAL and counterintuitive: an RX-888 with no firmware loaded sits in FX3 DFU/bootloader mode and enumerates at USB2 (480M) BY DESIGN — it only re-enumerates to USB3 (5000M) AFTER firmware is uploaded. A '480M' reading on a fresh device is NOT a USB3 fault, it's firmware-not-loaded-yet
This means Phase 1's RX-888 validation MUST upload firmware (rx888_stream -f SDDC_FX3.img) before it can prove anything — and it proves the rx888_stream code path, not radiod's, which gets proven separately in Phase 6.1
A recognized industry pattern, not unique to this project: USRP, bladeRF, and LimeSDR share this same firmware/FPGA-loading gap

## Slide 5
DESIGN RATIONALE
Key Design Decisions
Interactive device-selection menu — install only hardware you actually have connected, re-run any time to add more later
git/build-essential/cmake/pkg-config live in Phase 1, not Phase 2 — they exist specifically to build RX-888's from-source driver
usbfs_memory_mb raised for sustained USB3 streaming — required for the RX-888's high sample rates

## Slide 6
HANDS-ON
Hands-On Lab
1
sudo ./scripts/phase1-hardware-drivers.sh — select the devices you have connected
2
Reboot (NVIDIA driver, usbfs_memory_mb persistence, initramfs blacklist all require it)
3
./scripts/phase1-validate-sdrs.sh — confirm a real sustained capture for each SDR
4
./scripts/phase1-validate-protocol-tools.sh — confirm Ubertooth/Evil Crow RF if selected
5
Verify: cat /sys/module/usbcore/parameters/usbfs_memory_mb reads 1000, not 16

## Slide 7
REAL-WORLD BUG
Real Bug: The RX-888 'Stuck at USB2' Trap (a multi-day red herring)
The most instructive failure in this entire build. A brand-new RX-888 showed only USB2 (480M) in lsusb, never USB3 (5000M) — across every port on a Dell T5820, two cables, a BIOS audit (all settings already correct), and ultimately the purchase of a dedicated USB3 PCIe card. NONE of that was the cause. The RX-888 sits in Cypress FX3 DFU/bootloader mode (04b4:00f3, 'DFU mode') until firmware is loaded, and in that state it enumerates at USB2 BY DESIGN. The Phase 1 validation script was ALSO buggy — it never passed the -f firmware flag, so it couldn't trigger the re-enumeration. Once firmware was uploaded, the device jumped to USB3 and streamed 486 MB in ~8 seconds (~60 MB/s, physically impossible over USB2 — proof positive). The lesson: a symptom that looks like a hardware/host problem can be a device-state problem entirely, and confident wrong diagnoses ('it must be the port') can burn days. Also note: the device returns to DFU mode only on a real power cycle, so back-to-back validation runs fail with LIBUSB_ERROR_NO_DEVICE unless you reboot/replug first. (Bonus real bug from the same phase: 'apt install librtlsdr0' failed — renamed to librtlsdr2 in 24.04 — and usbfs_memory_mb via modprobe.d was silently ignored because usbcore is built statically into this kernel; fixed with a GRUB boot parameter.)

## Slide 8
BEFORE MOVING ON
Exit Criteria
Each selected SDR produces a real, sustained data capture, not just device enumeration
usbfs_memory_mb persists across a reboot
Ubertooth (if selected) shows firmware version and a live capture window

## Slide 9
GROUP DISCUSSION
Discussion Questions
Q1
The RX-888 'USB2 problem' was really a device-state problem. How do you build a diagnostic discipline that catches a wrong assumption before it costs you days of chasing the wrong layer?
Q2
Why does a device that enumerates at USB2 in DFU mode, then USB3 after firmware, defeat every port/cable/BIOS test you could run beforehand?
Q3
Why does a shared driver library (HackRF/RTL-SDR) create a different risk profile than a device-specific firmware-loading codebase like RX-888's?

## Slide 10
NEXT SESSION
Phase 2 — OS Packages: rootless Podman, FFTW background wisdom generation, and the Python venv strategy for the rest of the build.