## Slide 1
LAB 7
Phase 6.2 — Decode Layer
GNU Radio, direwolf, multimon-ng, and the venv boundary
Sovereign SIGINT — College Lab Series

## Slide 2
SESSION OVERVIEW
Learning Objectives
1
Install GNU Radio and its SDR abstraction layer (gr-osmosdr)
2
Understand why GNU Radio runs under system Python, not either project venv
3
Confirm this layer with a real flowgraph, not just a package-install check

## Slide 3
CONCEPT
What This Layer Provides
GNU Radio: the general-purpose DSP framework used later for occupancy-detection flowgraphs
gr-osmosdr: the abstraction layer letting GNU Radio talk to HackRF, RTL-SDR, and many other SDRs through one consistent interface
direwolf: packet radio / AX.25 / APRS software modem, also used for maritime AIS decode
multimon-ng: FLEX, POCSAG, and other digital-mode decoders

## Slide 4
SYSTEM DESIGN
The System-Python Boundary
GNU Radio's Python bindings are wired into system dist-packages by its apt package — not installable via pip into either project venv
Neither the ai-ingest nor sigint-processing venv was created with --system-site-packages, so GNU Radio's bindings are invisible to them by design
The practical split: GNU Radio flowgraphs run under system Python; anything that just CONSUMES GNU Radio's output (files, multicast streams) stays in the venv-isolated world
This decision, made all the way back in Phase 2, is exactly what makes the occupancy-detection flowgraphs in Phase 6.6 straightforward to write later

## Slide 5
DESIGN RATIONALE
Key Design Decisions
Installed BEFORE OpenWebRX+ (Phase 6.4) deliberately — OpenWebRX+ auto-detects direwolf and multimon-ng as optional decoders at its own startup, so order matters
Validation must build and run an ACTUAL flowgraph (a real source-to-sink data path), not just confirm the packages installed
ffmpeg included here for format conversion needs elsewhere in the pipeline

## Slide 6
HANDS-ON
Hands-On Lab
1
sudo ./scripts/phase6-decode-tools.sh
2
./scripts/phase6-decode-tools-validate.sh — builds and runs a real GNU Radio flowgraph, checks direwolf/multimon-ng/ffmpeg
3
Confirm GNU Radio's Python import works from system Python: python3 -c 'import gnuradio'
4
Confirm it does NOT import from either project venv (this is expected and correct)

## Slide 7
REAL-WORLD BUG
Why Validate With a Real Flowgraph
It would be easy to consider this phase 'done' once apt reports gnuradio installed successfully. But a package installing cleanly says nothing about whether its Python bindings are actually reachable, whether gr-osmosdr correctly finds the SDR hardware, or whether the whole dependency chain (Qt, VOLK, Boost) resolved without conflict. This build's validation script instead constructs and runs an actual signal source connected to an actual signal sink — a minimal but real, working flowgraph. If that runs, the entire chain is proven end to end. This is the same 'prove it with a real capture, not an enumeration' principle from Phase 1, applied to software instead of hardware.

## Slide 8
BEFORE MOVING ON
Exit Criteria
A real GNU Radio flowgraph builds and runs successfully
direwolf and multimon-ng both report their version correctly
ffmpeg completes a real encode test

## Slide 9
GROUP DISCUSSION
Discussion Questions
Q1
Why might 'the package installed' and 'the software actually works' be two very different claims, especially for a large DSP framework?
Q2
What are the tradeoffs of the venv-isolation decision made in Phase 2, now that we see its consequence here?
Q3
Could you restructure this build to avoid the system-Python/venv split entirely? What would you give up?

## Slide 10
NEXT SESSION
Phase 6.3 — SigID Mirror: a local reference catalog, and a rate-limiting bug that killed an entire sync run.